## Slide 1: Medicine Delivery Robot
Kevin Blount
Anthony Dietz
Brock Stechschulte

## Slide 2: Problem Statement:
For our project we are tackling the problem of how hard it is for senior citizens receive their medications in their own home. To resolve this problem, we are creating The Medicine Delivery Robot. This robot will deliver a person’s medicine to them wherever they are in their home.

## Slide 3: Areas of Research
Looked at robotic systems used both in the hospital, and systems used commercially in other areas of our daily lives
Current technologies show that we are moving towards more sophisticated robotic devices
These devices are able to navigate complex, sometimes unpredictable, floor plans
  Hospital building with multiple levels with different layouts

## Slide 4: Tug
Developed by Aethon
Fully autonomous hospital robot
  Delivers food and medicine to different parts of the hospital
Uses LiDAR sensors to create 3D map of its surroundings
Comes in different variants:
  T3, T3XL, The Drawer
Can be monitored all around the world by Aethon’s control centers
Max Payload: Depends on variation, starts at 1,000 lbs
Battery Life: 10 hrs

## Slide 5: Hospi
Being developed in Japan
Comes pre programmed with map of the hospital
Uses this information along with Ultrasonic sensors to navigate
Features onboard security
  Need a key card to access the contents that you ordered
Max payload: 45lbs
Battery Life: 9 hrs

## Slide 6: Roomba
The roomba is the most used household robot on the market today.
This robot can navigate a home and maneuver around obstacles to complete its task.
This robot is small and compact and returns to the charging station located in the house.

## Slide 7: Relay Robot
This robot was developed by the company Savioke.
This Robot has the capability to securely deliver food medicine or groceries to people in need.
These robots can be found in hotels, hospitals and other crowded areas
Very secure so items do not get stolen on the way

## Slide 8: End User
So who would be most likely to use our product?
We are targeting those who have a difficult time moving around their homes or who have trouble remembering to take their medication
Currently, the number of skilled nursing homes are on a decline in the US (20% less by 2020)
  This means that more and more people who need help, aren’t getting it
  Hard for caregivers (nurses and family members) to keep up with needs

## Slide 9: Sample Survey

## Slide 10: House of Quality (HoQ)

## Slide 11: Survey & HoQ Results
Customer Features
Alarms (4.33)
Lights (4.00)
Interchangeable Storage Units (3.48)
Camera (3.41)
Engineering Characteristics
User Interface (4.7)
Mobility (4.1)
Battery Life & Storage (3.9)
Overall Size (3.7)
Appeal (3.6)
Relative Weighting
Battery Size/Type - 17.0%
Mobility- 3.6%
Medicine Storage Capacity- 3.4%
User interface- 3.4%
Size- 6.5%
Motors - 16.3%
Sensors - 6.4%
Design - 16.6%
Materials - 24.9%

## Slide 12: What we need to build
A robot that can navigate a person's home to bring them medication
  Sensors that allow it to sense objects in its path (ie. Clothes, box, etc.)
Needs an alarm to alert user of its presence or any problems
Must be at average waist height so user doesn’t have to bend down
Intuitive interface that can be easily navigated
Mobility and battery life that allows this to not be an inconvenience
The overall look was not a big issue, convenience outweighs appeal
A camera was not deemed necessary in the initial design.
  Can be integrated into future products

## Slide 13: Design Concept 1
Car design. Could be wheeled or tracked
Pros:
More agile (able to climb over objects)
Less likely to get hung up on clutter (clothes, small objects)
Lighter, needs less power
Cons:
Short (user would have to bend over)
If wheeled, would have a larger turn radius

## Slide 14: Design Concept 2
Short disk (think roomba)
Pros:
Compact
Less expensive
Cons:
User has to bend down to retrieve their medicine
Limited features

## Slide 15: Design Concept 3
Tower concept with two wheels to drive the robot, swivel caster in the rear for stability
Pros:
Can reach waist height easily
Storage compartment is within arms reach
Cons:
Higher center of gravity
Takes up more space

## Slide 16: Final Design
Went with tower design
Allows more space for features
  Alarm
  Sensors
  Indexing storage
  Water bottle storage

## Slide 17: Final Design Sectioned
Placed motors, battery, and CPU in base to lower center of gravity
Material
  ABS plastic
  PVC piping
  Baltic Birch wood

## Slide 18: Final Design Dimensions
Weight (only ABS): 12.96 lbs
Total Weight: 36 lbs

## Slide 19: Drive Base Design
Features Hexagon holes in wall
  Saves weight
  Air flow for cooling
Cut out sections for wheels
  2 five inch slots for wheel
  1 cut out section for swivel wheel
Hole locations
  Raspberry pi 3B+ Standoffs
  Motor mounts
  Axle Mounts
  Gearbox mount
  Swivel wheel mounts

## Slide 20: Drive Base Design With Motors and Sensors

## Slide 21: Base` Lid Design
0.472 in thick - 13.68 lb*f applied - Max Deflection .0004in

## Slide 22: Tower Designs
Middle Tower
Lid / Alarm Tower
Upper Tower

## Slide 23: Drink Holder Design
Max Deflection .000258 in
1.39lb*f
.46 lb*f per cup holder

## Slide 24: 3D Printing
Printing out of the Digital Fabrication Lab @ Victory Parkway Campus, University of Cincinnati
  Great quality with their prints
Better prices compared to 1819 Innovation Center

## Slide 25: 3D Printer
Using the SST 1200es series printer
FDM Printer
Prints ABS plastic
Build Tray Size: 254 x 254 x 305 mm (10 x 10 x 12 in)
Layer Resolution: 0.254 mm (0.010 in)

## Slide 26: Order of Printing
Print the Drive Base and Indexing components first
  Connected to motors
  Most crucial, Other sections can be printed as we wire/code the motors

## Slide 27: Indexing Mechanism
Gearing:
Has a 30:1 gear reduction
Uses a standard vertical gear attached to a horizontal worm gear
Motor:
Powered by 12V motor
  200 rpm (no load)
  ~7 rpm with reduction
Has an encoder shaft in order to track the rotations

## Slide 28: Medicine Storage
Circular indexing storage compartment
Indexes each time a new set of medication is ready

## Slide 29: Indexing Motor Testing

## Slide 30: Force Calculations
Desired Speed 3.1mph (Standard Walking)
Total weight of robot 40lbs
Safety factor 1.5
Safety factor weight 60 lbs
Incline 4.8° (maximum wheelchair incline)
Coefficient of friction = 0.8 (Grip material for handicap ramps)
Fa = Force applied to get robot up ramp
Fa = 26.43 * 2 motors = 52.86 lbs*ft

## Slide 31: Power and Torque Calculations
Power Calculation for One Motor:
Power = Force * Velocity
Force = Fa = 26.43 lbs*ft
Velocity = 4.54 ft/s
Power = 119.97 lbs*ft/s
Power = 0.218Hp
Torque Calculation for one wheel:
Torque = Force * radius
Radius = 2.5in
Force = 26.43 lb*ft
Torque = (26.43)*(2.5/12) = 5. 51 lb*ft

## Slide 32: Motor Selection Groschopp 24V DC Brushless Motor 7122
Speed: 2,900 rpm
Torque: 4.4 in-lb (70.4in-oz)
Power: 0.2 hp
Will use encoder for positioning feedback
This motor is compact while delivering more than the required power needed!

## Slide 33: Gear Train Calculations and Selection

## Slide 34: Circuit Diagram

## Slide 35: Ultrasonic Sensors
Parallax PING Ultrasonic Sensor
20mA
Total of 3 Sensors:
  1 Mounted straight ahead
  2 Mounted at 45 degrees
Sensing range of 2 cm - 3m

## Slide 36: Ultrasonic Sensors Testing (Object Far)
When an object is far enough away that it won’t interfere with the robot, the sensors simply record its distance and the robot continues on its path

## Slide 37: Ultrasonic Sensors Testing (Object Near)
When an object gets too close to the robot, they read a -1 value and show a “Low” warning. This tells the robot that it is about to collide with an object and needs to stop and swivel around the object in order to complete it’s path

## Slide 38: Alarm
Large Piezo Alarm
2-18 V dc
  No resistor
Puts out 100 dB @ 3KHz
  Equivalent to average motorcycle
Alerts user when it arrives with medicine
  If it becomes stuck
  Whatever assistance it needs

## Slide 39: Battery Selection
Two 12 volt 9 Ah batteries wired in series to get the desired voltage for the drive motors
One 12 volt 2 amp battery pack to meet the requirement to power the indexing motor

## Slide 40: Development
At its core, the Medicine Delivery Robot is controlled by a Raspberry Pi. When powered on, the Raspberry Pi deploys the web application which allows the user to start the medicine delivery process. It also controls the motors, sensors, alarm, and medicine dispensing mechanism.

## Slide 41: Raspberry Pi 3B+ Control Board
1.4GHz 64-bit quad core processor
  The brains of our robot
5V & 2.5A DC power input
  Will receive power from separate batteries
Micro SD card to load our programs
Programmed using Java

## Slide 42: User Interface

## Slide 43: How it works
Connect the Robot to your Wifi
Go to the IP address connected to the robot
Set up delivery time and medicine

## Slide 44: How it works
If you do not have any times scheduled, it will show a message saying:
“You don’t have any times for delivery setup. You can schedule delivery times using the above option”

## Slide 45: Delivery of Medicine

## Slide 46: Animation of Robot

## Slide 47: Budget
Total Amount
: $3,861.33 or $1,287.11 per teammate

## Slide 48: Final Results
Unable to complete
However, due to COVID-19, we were not able to complete the construction of our robot. Many of the parts that we required were not able to be 3D printed with 3D print labs shutting down. We also weren’t able to cut our PVC pipe and lids to fit our robot. Finally, we were unable to order our motor controllers as they were from China and could not be delivered.
Accomplished
Creating a unique design which accommodates all end user’s demands.
Development and wiring of the hardware items (index motor, sensors, alarms) to the Raspberry Pi.
Creating a user interface that is deployed when the robot is powered on.
Partial construction of our robot’s base and medicine dispenser.

## Slide 49: Future Implementations
Complete the construction of the medicine delivery robot.
Improvements to the design of the web application.
Create automated message system to notify care takers when they need to refill the medicine dispenser.
Add new features such as Camera, AI system, and a locator device

## Slide 50: Citations
1. Samadi, David D. History and the future of Robotic Surgery. Robotic Oncology. [Online] [Cited: Sep 05, 2019.] https://www.roboticoncology.com/history-of-robotic-surgery/.
2. Tug, the Busy Little Robot Nurse, Will See You Now. Wired. [Online] May 25, 2018. [Cited: Sep 05, 2019.] https://www.wired.com/story/tug-the-busy-little-robot-nurse-will-see-you-now/.
3. The TUG Autonomous Robot. Aethon. [Online] [Cited: Sep 05, 2019.] https://aethon.com/mobile-robots-for-healthcare/.
4. Panasonic Autonomous Delivery Robots - HOSPI - Aid hospital Operations at Changi General Hospital. Panasonic Newsroom. [Online] Panasonic Corporation, Jul 23, 2015. [Cited: Sep 05, 2019.] https://news.panasonic.com/global/topics/2015/44009.html.
5. Hospi. Wikipedia. [Online] Aug 16, 2019. [Cited: Sep 05, 2019.] https://en.wikipedia.org/wiki/Hospi.